## Slide 1
Intelligent Monocular Forward-Vision System (IMFS)

## Slide 2
Hritik
Jhaveri
Anubuthi Kottapalli
Meet Our Team
Deepali Dagar
Ashwin Ram Venkataraman
2

## Slide 3
Client and Business Statement
Our Product - IMFS
Model in Action
Data is Everything
Future Development & Client Statement
1
Agenda
3
2
3
4
5

## Slide 4
Kevin Stutenberg leads the project, with Michael Pamminger and Yihe Chen providing technical research and implementation.
Argonne National Laboratory, one of the U.S. Department of Energy’s 17 national labs, is engaged in cutting-edge research in energy, transportation, and national security. This project is done in collaboration with Connected and Automated Vehicle (CAV) research.
Advanced Computing & AI
Energy Innovation
Cross-Disciplinary Scientific Research
Business Problem
Data Assesment
Client
Our
Product
Model In Action
Limitations
Future
Scope
4

## Slide 5
Business Statement
The Problem
Accurate vehicle distance measurement is key to studying driver behavior, but high LiDAR/RADAR costs limit research.
The Opportunity
Provide a scalable, accessible solution that delivers reliable real-time distance estimation using monocular video from common hardware like dash-cams.
Business Problem
Data Assesment
Client
Our
Product
Model In Action
Limitations
Future
Scope
5

## Slide 6
Business Problem
Data Assesment
Client
Our
Product
Model In Action
Limitations
Future
Scope
6
Strategic Opportunity & Project Goals
Core Project Goals
  Estimate distance to lead car to understand driver behavior.*
  Design and benchmark a lightweight, real-time AI model.
  Target metrics:
    close to real time
    model size (<100 MB)
    Absolute error ~ 2.00 m *

## Slide 7
What We Achieved
Business Problem
Data Assesment
Client
Our
Product
Model In Action
Limitations
Future
Scope
7
Notes: 7

## Slide 8
Fully Processed Image
Raw Image
Undistorted Image
Business Problem
Data Assesment
Client
Our
Product
Model In Action
Limitations
Future
Scope
Raw monocular dash-cam frame
Lens distortion removed & perspective
straightened for accurate geometry.
Brightness/contrast normalized
Model in Action: Preprocessing
8

## Slide 9
ROI Polygon
  Restricts detection to the drivable area, emphasizing the lead vehicle zone.
YOLO - Real Time Object Detection Algorithm
  Detects vehicles in real time and provides accurate bounding boxes for the lead vehicle.
Center Focus
  Gives priority to vehicles near the vertical center to isolate the true lead vehicle.
Bottom-Crop Heuristic
  Removes the bottom 20% of the frame to avoid hood reflections, occlusions, and irrelevant foreground clutter.
Our
Product
Business Problem
Data Assesment
Limitations
Future
Scope
Client
Model In Action
9
Model in Action: Lead Vehicle Detection

## Slide 10
Business Problem
Data Assesment
Our
Product
Limitations
Future
Scope
Client
Model In Action
10
Model in Action: Model Selection

## Slide 11
  Bounding box geometry (width, height, and aspect ratio)
  Position (vertical and horizontal) of lead vehicle
Our
Product
Full Image
Car Patch
Final Ouput
Geometric
Features
Business Problem
Data Assesment
Limitations
Future
Scope
Client
Model In Action
11
Model in Action: Distance Estimation

## Slide 12
  Argonne National Lab dataset - PII filtered, proprietary
  19,000+ images across LA, Nashville, Chattanooga
  Ground truth distances encoded in filenames
Raw Dashcam Image
Dataset Distribution
  Heavy concentration in 0-30m range - reflects typical city driving patterns
  Critical safety range underrepresented - only 4.8% of samples under 2m
  Long-range samples (>40m) are limited
Business Problem
Data Assesment
Our
Product
Model In Action
Limitations
Future
Scope
Client
12
Understanding Our Data

## Slide 13
Weather, lighting, and blur augmentations applied
Better Generalization compared to Synthetic CARLA Data
Model In Action
Method 1: Simulated data
Method 2: Augmentation
  CARLA simulator used to generate balanced distance samples
  Synthetic-to-real domain gap too large - model failed to generalize from simulated to real dashcam images
Business Problem
Our
Product
Limitations
Future
Scope
Data Assesment
Client
13
Improving Our Data

## Slide 14
A single camera lacks true depth perception, making distance an estimation rather than a precise measurement (unlike Stereo Vision, RGBD camera, LiDAR)
CAMERA OUTPUT
LiDAR OUTPUT
RGB-D OUTPUT
Business Problem
Data Assesment
Our
Product
Model In Action
Future
Scope
Limitations
Client
14
Monocular Vision Ambiguity

## Slide 15
Sharp Turns
Extreme Light & Weather conditions
Business Problem
Data Assesment
Our
Product
Model In Action
Future
Scope
Limitations
Client
15
Edge Cases

## Slide 16
Future Improvements
Business Problem
Data Assesment
Our
Product
Model In Action
Future
Scope
Limitations
Client
16
• Multi‑modal Input (Vision + Vehicle Control Signals)
Fuses camera data with vehicle dynamics for robust perception.
• Temporal / Multi‑frame Inference
Leverages sequential frames to improve distance estimation accuracy.
• Adaptive Depth Estimation
Dynamically adjusts predictions for varying road and traffic conditions.

## Slide 17
Client Statement
17

## Slide 18
Thank you!

## Slide 19
Appendix
19

## Slide 20
MODEL ARCHITECTURE
20

## Slide 21
INFERENCE OUTPUT
21

## Slide 22
MODEL EVALUATION
22